## Slide 1: FEASIBILITY ANALYSIS AND PERFORMANCE TESTING OF COLLISION DETECTION ALGORITHMS FOR SATELLITES
Capstone Project Phase B
23-2-D-17
Hallel Weil
Omer Shamir
Supervisor: Mr. Ilya Zeldner

## Slide 2: Introduction
Satellites
Space debris
Finding possible collisions
Implementing on a satellite on-board computer
Active\Old Satellites, Space debris
Active satellites[orange]
Inactive satellites[Blue]
Space debris[Grey]
Rocket bodies[purple]
Uncategorized[pink]

## Slide 3: Introduction
Finding the minimal distance
Small time step
Approximations using polynomials

## Slide 4
ANCAS
SBO ANCAS
CATCH
Algorithms

## Slide 5
Implemented, tested and ready to use algorithms
Testing system
Experiments result, feasibility of using the algorithms on satellites
Expected result

## Slide 6
Implementing the algorithms
2 Parts testing system
Comparing algorithms performance
Solution

## Slide 7: Algorithms Implementation
Implemented in C++
Eigen for finding eigenvalues
Unit test and CelesTrak + SOCRATES

## Slide 8: Testing System
2 parts testing system
Testing station
Tested on-board computer
User Interface
Test Creation and Management
Results Management
Database
Running tests
Running the algorithms
Testing runtime

## Slide 9: Testing System
Testing station
Tested on-board computer

## Slide 10: Testing System - Communication
Defining a communication protocol
Error detection - CRC
Work on:
UDP
TCP
Local simulation

## Slide 11: Testing System – Environments - Windows
Windows / WSL
TCP/UDP over Local host
Local simulation

## Slide 12: Testing System - Environments – RP4
Linux on Raspberry Pi 4
TCP/UDP
Testing Cross – Platform Communication

## Slide 13: Testing System – Environments - Simulation
gem5 simulation
Open source, Community led project
Framework for computer systems simulations
Accurate timing

## Slide 14: Testing System – Activity Diagram

## Slide 15: Feasibility Testing Environments
gem5 simulator with WSL
Simulation script - se
 | OBC | gem5 simulation script
CPU | 32-bit ARM9 | SimpleTimingCPU
CPU Frequency | 400MHz | 400MHz
Cache | 32-KB Data, 32-KB Instruction | 32-KB Data, 32-KB Instruction
Memory | 32MB SDRAM | SimpleMemory

## Slide 16
Catalog of objects from Celestrak - 9727 active satellites
Used around 20% - ~5700 tests
3 days to run the simulation
Feasibility testing - data

## Slide 17
Feasibility testing - runtime

## Slide 18
Feasibility testing - errors
Algorithm | Average Runtime[Sec] | Average Distance Error[KM] | Average #Points | Test With Distance Error > 0.00001[KM] | Test With Distance Error > 0.100[KM]
ANCAS | 0.026057568 | 0.222462893 | 3019 | 1902 | 783
SBO ANCAS | 0.159591541 | 0.007744792 | 3019 | 91 | 8
CATCH | 0.663982872 | 0.022729184 | 3019 | 41 | 12

## Slide 19
Feasibility testing – correlations
Constant time interval- changing number of points

## Slide 20
Feasibility testing – correlations
Constant number of points – changing time interval

## Slide 21: Challenges
Developing for unknown / multiple systems
  Types
  Padding
  Different functions
Testing and debugging
  Unit tests
  Local Simulations
  Loggers

## Slide 22: System Testing
Unit tests
Local Simulation with test cases
RP4 cross platform communication testing
Acceptance testing

## Slide 23: User Interface – Video

## Slide 24: User Interface – Home Page

## Slide 25: User Interface – Create Test

## Slide 26: User Interface – Test Results

## Slide 27: Bibliography
[1] Denenberg, Elad. "Satellite closest approach calculation through Chebyshev Proxy Polynomials." CATCH
[2] Alfano, S. "Determining Satellite Close Approaches-Part II." ANCAS
[3] Denenberg, Elad. Gurfil, Pini. “Improvements to Time of Closest Approach Calculation.” SBO ANCAS
[4] NASA on orbital debris: NASA
[5] CelesTrak: https://celestrak.org/
[6] CelesTrak Current Data: https://celestrak.org/NORAD/elements/index.php?FORMAT=tle
[7] The gem5 simulator: https://www.gem5.org/
[8] ISISPACE OBC: https://www.isispace.nl/product/on-board-computer/
[10] Our GitHub repository: https://github.com/ommersh/Final-Project